## Slide 1: BIOCIDAL PRODUCTS REGULATION
AUTOMOTIVE INDUSTRY RECOMMENDATIONS
Jonathan Swindell Chair, Task Force-BIOCIDES
22 April 2015

## Slide 2: Overview
Biocidal Products Regulation (BPR)
  Came into force on 1 September 2013
  Sets rules in the EU for:
    Active substance approval
    Biocidal products authorisation
    Placing treated articles on the market
  Includes transitional measures from the previous Biocidal Products Directive (BPD)
  Automotive industry vehicle manufacturers and the many tiers of the supply chain can have multiple roles & obligations under BPR
  Task Force-BIOCIDES recommends 10-Step Compliance
ACTIVE SUBSTANCE (AS) – substance or micro-organism that has an action on or against harmful organisms
BIOCIDAL PRODUCT (BP) – substance or mixture containing one or more active substances, with the intention of controlling harmful organisms by means other than mere physical or mechanical action
TREATED ARTICLE (TA) – substance, mixture or article which has been treated with, or intentionally incorporates, one or more biocidal products
PRODUCT-TYPE (PT) – ASs are approved for specific PTs; BPs and TAs are allowed on the market only if all the active substances concerned are approved for the relevant PTs

## Slide 3: STEP 1: Identify Biocidal Products & Treated Articles
Treated Article (TA) | Biocidal Product (BP) | Neither TA nor BP
“Article” is treated short term with biocidal product(s) |  | ”Article” unintentionally comes into contact with BP or TA (e.g. machined part in contact with treated metalworking fluid)
“Article” intentionally incorporates biocidal product(s), and has a (non-primary) biocidal function relevant to finished good (e.g. odour control in air-conditioning systems) | “Article” intentionally incorporates biocidal product(s), and has a primary biocidal function | “Article” intentionally incorporates active substance but not for its biocidal property (e.g. thiram as a vulcanising agent)
“Mixture” intentionally incorporates biocidal product(s), but does not have a biocidal function relevant to finished good (e.g. paint with in-can preservative) | “Mixture” contains an Active Substance and has a biocidal function relevant to finished good (e.g. anti-microbial additive for metalworking fluids) | “Mixture” intentionally incorporates active substance but not for its biocidal property

## Slide 4: STEP 2: Identify Product-Types
Product-Type |  | Arguments in favour | Arguments against
PT2 | Disinfectants and algaecides not intended for direct application to humans or animals | Mentions air conditioning systems | PT2 is under the Main group 1: Disinfectants, and applies to short term treatment of existing micro-organisms
PT7 | Film preservatives | PT7 is under Main Group 2: Preservatives, and covers “… products to prevent microbial and algal development”. | PT7 refers to use of biocidal products “…for the preservation of films or coatings…” but does no cover prevention of odour build-up.
PT9 | Fibre, leather, rubber and polymerised materials preservatives | PT9 is under Main Group 2 and covers “… biocidal products which antagonise the settlement of micro-organisms on the surface of materials and therefore … prevent the development of odour…”. | PT9 scope does not include metallic articles.
PT11 | Preservatives for liquid-cooling and processing systems | PT11 refers to “ …the preservation of water or other liquids …”. | PT11 refers to “Preservatives for liquid-cooling and processing systems”.
E.g. A/C Core intentionally incorporates an active substance on its outer surface to preventing the build-up of micro-organisms on the surface in order to avoid odours in the A/C system:

## Slide 5: STEP 3: Identify Roles and Obligations
Your obligations depend on whether you:
  Place Biocidal Products on the market
  Placing Treated articles on the market
  Use biocidal products
  Create and use Biocidal Products in situ
How you meet your obligations depends on whether you:
  Manufacture Biocidal Products or Treated Articles
  Import Biocidal Products or Treated Articles
  Are a downstream user of Biocidal Products or Treated Articles

## Slide 6: STEP 4: Check Active Substances Status
USE OF BIOCIDAL PRODUCT: Check AS/PT Approval | Conclusion
AS is on the Annex I list under Categories 1 to 5 or 7 | AS may be used in BP for all PTs
AS is on Annex I under Category 6, and supplier is on the Article 95 List for the AS/PT | AS may be used in BP for the specified PT
AS/PT is on the Union List, and supplier is on the Article 95 List for the AS/PT | 
None of the above conditions apply | AS may not be used in a BP after 1 Sept 2015
MARKETING OF TREATED ARTICLE: Check AS/PT Approval | Conclusion
AS is on the Annex I list | TA may be marketed without time limit
AS/PT is on the Union List | 
AS/PT is on the Work Programme (i.e. application for AS/PT approval made before 1 Sep 2016) but no decision yet | TA may be marketed, pending approval decision
Non-approval decision is made for the AS/PT after 1 Sep 2016 | TA may not be marketed after 180 days after Rejection
Non-approval decision is made for the AS/PT before 1 Sep 2016 | TA may not be marketed after 1 Mar 2017, unless a new application is approved
None of the above conditions apply | 

## Slide 7: STEPS 5, 6 & 7: Obligations related to Labelling
STEP 5: Comply with Active Substance Approval Conditions
  Check conditions of Active Substance approvals on the ECHA website.
  Approval conditions could include requirements for labelling of Biocidal Products or Treated Articles.
STEP 6: Identify Claims made for Treated Articles
  For BPR labelling requirements, a “claim” is any statement that indicates or implies that the treated article has either:
    Protection against unwanted organisms (i.e. a biocidal property only); or,
    Action against unwanted organisms (i.e. a biocidal function).
STEP 7: Label Treated Articles as Required
  Labelling is required for Treated Articles placed on the market if either:
    Conditions of the substance approval include a labelling requirement.
    A claim is made regarding biocidal properties of the Treated Article; or,
  Labelling may include biocidal property attributed to the treated article only if substantiated

## Slide 8: STEPS 8, 9 & 10: Follow-Up Obligations
STEP 8: Provide Information to Customers on Request
  On request from a customer, the supplier must provide information about the biocidal treatment on the treated article, free of charge, within 45 days.
  Automotive industry requires declaration in IMDS of Active Substances, when intentionally incorporated for their biocidal properties.
STEP 9: Substitute/Eliminate Active Substances
  In case your use of an Active Substance in a Biocidal Product or Treated Article is not approved, work with your suppliers and customers to ensure substitution according to transitional deadlines.
STEP 10: Maintain Records
  Records may be requested by Authorities in case of audits, legal cases, etc.

## Slide 9: 10 Recommended Steps
1. Identify Biocidal Products & Treated Articles
2. Identify Product-Types
3. Identify Roles and Obligations
4. Check Active Substances Status
5. Comply with Active Substance Approval Conditions
6. Identify Claims made for Treated Articles
7. Label Treated Articles as Required
8. Provide Information to Customers on Request
9. Substitute/Eliminate Active Substances
10. Maintain Records
… TO COMMUNICATE WITH YOUR SUPPLIERS AND WITH YOUR CUSTOMERS ABOUT BIOCIDES!
AND AS ALWAYS THE MOST IMPORTANT THING IS …

## Slide 10: Automotive Industry Guideline on BPR
COMING SOON …

## Slide 11: THANK YOU
Jonathan Swindell
  Product Stewardship Manager
  M +44(0)7552 286 602
  jswinde1@jaguarlandrover.com